## Slide 1: Number system

## Slide 2
Common Number Systems
System | Base | Symbols | Used by humans? | Used in computers?
Decimal | 10 | 0, 1, … 9 | Yes | No
Binary | 2 | 0, 1 | No | Yes
Octal | 8 | 0, 1, … 7 | No | No
Hexa- decimal | 16 | 0, 1, … 9, A, B, … F | No | No

## Slide 3
counting
Decimal | Binary | Octal | Hexa- decimal
0 | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 10 | 2 | 2
3 | 11 | 3 | 3
4 | 100 | 4 | 4
5 | 101 | 5 | 5
6 | 110 | 6 | 6
7 | 111 | 7 | 7

## Slide 4
Conversion Among Bases
The possibilities:
Decimal
Octal
Binary
Hexadecimal

## Slide 5
Binary to Decimal
Decimal
Octal
Binary
Hexadecimal

## Slide 6
Binary to Decimal
Technique
  Multiply each bit by 2n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 7
Example
1010112 => 1 x 20 = 1 1 x 21 = 2 0 x 22 = 0 1 x 23 = 8 0 x 24 = 0 1 x 25 = 32
4310
Bit “0”

## Slide 8
Octal to Decimal
Decimal
Octal
Binary
Hexadecimal

## Slide 9
Technique
  Multiply each bit by 8n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 10
Example
7248 => 4 x 80 = 4 2 x 81 = 16 7 x 82 = 448 46810

## Slide 11
Hexadecimal to Decimal
Decimal
Octal
Binary
Hexadecimal

## Slide 12
Hexadecimal to Decimal
Technique
  Multiply each bit by 16n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 13
Example
ABC16 => C x 160 = 12 x 1 = 12 B x 161 = 11 x 16 = 176 A x 162 = 10 x 256 = 2560
274810

## Slide 14
Decimal to Binary
Decimal
Octal
Binary
Hexadecimal

## Slide 15
Decimal to Binary
Technique
  Divide by two, keep track of the remainder
  First remainder is bit 0 (LSB, least-significant bit)
  Second remainder is bit 1
  Etc.

## Slide 16
Example
12510 = ?2
2 125 62 1
2 31 0
2 15 1
2 7 1
2 3 1
2 1 1
2 0 1
12510 = 11111012

## Slide 17
Octal to Binary
Decimal
Octal
Binary
Hexadecimal

## Slide 18
Octal to Binary
Technique
  Convert each octal digit to a 3-bit equivalent binary representation

## Slide 19
Example
7058 = ?2
7 0 5
111 000 101
7058 = 1110001012

## Slide 20
Hexadecimal to Binary
Decimal
Octal
Binary
Hexadecimal

## Slide 21
Hexadecimal to Binary
Technique
  Convert each hexadecimal digit to a 4-bit equivalent binary representation

## Slide 22
Example
10AF16 = ?2
1 0 A F
0001 0000 1010 1111
10AF16 = 00010000101011112

## Slide 23
Decimal to Octal
Decimal
Octal
Binary
Hexadecimal

## Slide 24
Decimal to Octal
Technique
  Divide by 8
  Keep track of the remainder

## Slide 25
Example
123410 = ?8
8 1234
154 2
8
19 2
8
2 3
8
0 2
123410 = 23228

## Slide 26
Decimal to Hexadecimal
Decimal
Octal
Binary
Hexadecimal

## Slide 27
Decimal to Hexadecimal
Technique
  Divide by 16
  Keep track of the remainder

## Slide 28
Example
123410 = ?16
16 1234
77 2
16
4 13 = D
16
0 4
123410 = 4D216

## Slide 29
Binary to Octal
Decimal
Octal
Binary
Hexadecimal

## Slide 30
Binary to Octal
Technique
  Group bits in threes, starting on right
  Convert to octal digits

## Slide 31
Example
10110101112 = ?8
1 011 010 111
1 3 2 7
10110101112 = 13278

## Slide 32
Binary to Hexadecimal
Decimal
Octal
Binary
Hexadecimal

## Slide 33
Binary to Hexadecimal
Technique
  Group bits in fours, starting on right
  Convert to hexadecimal digits

## Slide 34
Example
10101110112 = ?16
10 1011 1011
B B
10101110112 = 2BB16

## Slide 35
Octal to Hexadecimal
Decimal
Octal
Binary
Hexadecimal

## Slide 36
Octal to Hexadecimal
Technique
  Use binary as an intermediary

## Slide 37
Example
10768 = ?16
1 0 7 6
001 000 111 110
2 3 E
10768 = 23E16

## Slide 38
Hexadecimal to Octal
Decimal
Octal
Binary
Hexadecimal

## Slide 39
Hexadecimal to Octal
Technique
  Use binary as an intermediary

## Slide 40
Example
1F0C16 = ?8
1 F 0 C
0001 1111 0000 1100
1 7 4 1 4
1F0C16 = 174148

## Slide 41
Binary Addition
Two 1-bit values
A | B | A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 10
“two”

## Slide 42
Binary Addition (example)
Two n-bit values
  Add individual bits
  Propagate carries
  E.g.,
10101 21 + 11001 + 25 101110 46
1
1

## Slide 43
Multiplication
Binary, two 1-bit values
A | B | A  B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 44
Multiplication (example)
Binary, two n-bit values
  As with decimal values
  E.g.,
1110 x 1011 1110 1110 0000 1110 10011010

## Slide 45: Binary Subtraction
Have previously looked at the subtraction operation. A quick review.
Just like subtraction in any other base
  Minuend 10110
  Subtrahand - 10010
  Difference 00100
And when a borrow is needed. Note that the borrow gives us 2 in the current bit position.
.

## Slide 46: Binary Division
Binary division is also performed in the same way as we perform decimal division. Like decimal division, we also need to follow the binary subtraction rules while performing the binary division. The dividend involved in binary division should be greater than the divisor. The following are the two important points, which need to be remembered while performing the binary division.
If the remainder obtained by the division process is greater than or equal to the divisor, put 1 in the quotient and perform the binary subtraction.
If the remainder obtained by the division process is less than the divisor, put 0 in the quotient and append the next most significant digit from the dividend to the remainder.

## Slide 47: Binary Division
Perform the binary division of the decimal numbers 18 and 8.
The equivalent binary representation of the decimal number 18 is 10010.
The equivalent binary representation of the decimal number 8 is 1000.
1 | 0 | 0 | 0 | ) | 1 | 0 | 0 | 1 | 0 | ( | 1 | 0
 |  |  |  |  | 1 | 0 | 0 | 0 |  |  |  | 
 |  |  |  |  | 0 | 0 | 0 | 1 | 0 |  |  | 
 |  |  |  |  | 0 | 0 | 0 | 0 | 0 |  |  | 
 |  |  |  |  | 0 | 0 | 0 | 1 | 0 |  |  | 
Quotient
Remainder

## Slide 48: Signed/Unsigned Numbers
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 0 | 0 | 1 | 0
Sign bit
Sign bit
50
-50

## Slide 49: Signed/Unsigned Numbers
Advantages of the signed-magnitude representation:
It is very easy to represent and understand positive as well as negative numbers using this representation.
The binary multiplication and the binary division of the signed binary numbers can be easily performed.
Represent equal number of positive and negative quantities that makes it a very symmetrical method of representation.

## Slide 50: Signed/Unsigned Numbers
Disadvantages of the signed-magnitude representation:
1
It is not an easy task to perform the binary addition and the binary subtraction using this representation.
2
It provides two different representations of zero, one for plus zero and another for negative zero but actually they are the same values. This could lead to some confusion while performing various arithmetic operations.
3

## Slide 51: Complements of Binary Numbers
The complement system can also be used to represent the signed binary numbers apart from the signed-magnitude representation method.
In the complement system, the positive integers are represented in a similar manner as they are represented in the signed-magnitude representation. The following are the two most popular complement methods used in the computer system:
One’s complement
Two’s complement

## Slide 52: One’s Complement
One’s complement method can be used to represent negative binary numbers.
A negative number can be represented using one’s complement method by first computing the binary equivalent of the number and then changing all the zeros with ones and all the ones with zeros.
For example, the binary equivalent of the decimal number 15 is 00001111. Therefore, -15 can be represented using one’s complement method as 11110000.

## Slide 53: One’s Complement
The one’s complement method also uses the left most bit as the sign bit to indicate the sign of the number.
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
Sign bit
-15

## Slide 54: One’s Complement
The one’s complement method of representing signed numbers also has two different representations for the number, zero.
Integers | One’s complement representation
-7 | 1000
-6 | 1001
-5 | 1010
-4 | 1011
-3 | 1100
-2 | 1101
-1 | 1110
-0 | 1111
+0 | 0000
+1 | 0001
+2 | 0010
+3 | 0011
+4 | 0100
+5 | 0101
+6 | 0110
+7 | 0111

## Slide 55: One’s Complement
The equivalent binary representation of 25 is in byte size is 00011001.
Now, change all the zeros to ones and all the ones to zeros in order to obtain the ones complement representation: 11100110
Therefore, the one’s complement representation of -25 is 11100110.

## Slide 56: Two’s Complement
Two’s complement is the most widely used method for representing negative numbers in the computer system.
The two’s complement of the given integer can be obtained by adding 1 to the one’s complement of that number.
For example, the two’s complement representation of -15 can be obtained by adding 1 to 11110000, which is the one’s complement representation of -15. Therefore, the two’s complement representation of -15 is 11110001.

## Slide 57: Two’s Complement
The two’s complement method also uses the left most bit as the sign bit to indicate the sign of the number.
1 | 1 | 1 | 1 | 0 | 0 | 0 | 1
Sign bit
-15

## Slide 58: Two’s Complement
Integers | Two’s complement representation
-7 | 1001
-6 | 1010
-5 | 1011
-4 | 1100
-3 | 1101
-2 | 1110
-1 | 1111
-0 | 0000
+0 | 0000
+1 | 0001
+2 | 0010
+3 | 0011
+4 | 0100
+5 | 0101
+6 | 0110
+7 | 0111

## Slide 59: Two’s Complement
The equivalent binary representation of 33 in a byte is 00100001.
Now, change all the zeros to ones and all the ones to zeros in order to obtain the one’s complement representation: 11011110.
Add 1 to the 11011110.
Therefore, the two’s complement representation of -33 is 11011111.

## Slide 60
Fractions
Binary to decimal
10.1011 => 1 x 2-4 = 0.0625 1 x 2-3 = 0.125 0 x 2-2 = 0.0 1 x 2-1 = 0.5 0 x 20 = 0.0 1 x 21 = 2.0 2.6875

## Slide 61
Fractions
Decimal to binary
.14579 x 2 0.29158 x 2 0.58316 x 2 1.16632 x 2 0.33264 x 2 0.66528 x 2 1.33056
etc.
3.14579
11.001001...